## Slide 1: Birthday Problem
You will design a circuit that will display your birthday one digit at a time. (mmddyy)
You will switch from one digit to the next by assigning a number to each one of the digits in your birthday and using binary conversion to create the inputs necessary to create that assigned number in binary.
EX:
  0  000  m = 1
  1  001  m = 2
  2  010  d = 2
  .
  .
  etc.
When your inputs are set to 0, your first digit will be displayed.
When your inputs are set to 1, your second digit will be displayed.
…and so on.

## Slide 2: Don’t Care
There will be times when a certain combination of inputs will not occur during normal operation. Rather than placing a 1 or 0 for these outputs, we place an X to signify that we “don’t care” about this particular outcome.

## Slide 3: Don’t Care Example
You need to create a circuit that will display the 4 cardinal directions to indicate if the user should change directions. You assign 0 – No change, 1 – North, 2 – South, 3 – East, 4 – West.
These are the only 5 inputs you care about,
but you need 3 inputs to make a 4 in binary.
This means there’s going to be 8 input
combinations, 3 of which you don’t care about.
This is what your truth table should look like.
# | A | B | C | Out
0 | 0 | 0 | 0 | NC
1 | 0 | 0 | 1 | N
2 | 0 | 1 | 0 | S
3 | 0 | 1 | 1 | E
4 | 1 | 0 | 0 | W
5 | 1 | 0 | 1 | X
6 | 1 | 1 | 0 | X
7 | 1 | 1 | 1 | X

## Slide 4: Don’t Cares and Karnaugh Maps
When you make a Karnaugh map with Don’t Cares they act as a “wild card.” They can represent either a 1 or a 0 depending on what is most convenient for you.
Ex:

## Slide 5: 7-Segment Display
Used to display characters
Light up different LED segments to create the characters

## Slide 6: Displaying Numbers 0-9

## Slide 7: Naming the Segments
Each segment is named using the letters A-F
The decimal point is shorted to DP on design schematics

## Slide 8: Common Anode
Our 7-segment LEDs are common anode
  Share the same power source, NOT the same ground
To turn ON an LED, you need to shift a 0
To turn OFF an LED, you need to shift a 1

## Slide 9: Pin Diagram (for Logisim)
G F A B
E D C DP
Note that the Logisim
diagram does not require you
to power this element but you will
need to power it IRL.

## Slide 10: Pin Diagram (for circuit)

## Slide 11: Birthday Problem Instructions
Complete the Birthday Problem Worksheet on the HUB
Next, build your schematic using Logisim. You should have three inputs and their complements (NOTs) and 7 different outputs. Each output will be connected to its corresponding input on the seven segment display. Make sure you change it to “Active On High? No.”