## Slide 1: Creating a BCD to 7-Segment Display Driver

## Slide 2: Binary Coded Decimal (BCD)
Binary coded decimal is a shorthand used to represent binary numbers using 4bits (a nibble) per decimal digit.
Example: 9401 in BCD is 1001010000000001
9 4 0 1
1001 0100 0000 0001

## Slide 3: Non-AOI Gate Summary

## Slide 4: NANDS
!(AB)
What does the gate look like? What does the expression look like?

## Slide 5: NORS
!(A+B)
What does the gate look like? What does the expression look like?

## Slide 6: XORS
!AB + A!B
(A+B)(!A+!B)
A^B
A[+]B
What does the gate look like? What does the expression look like?

## Slide 7: XNORS
AB + !A!B
!(A^B)
!(A[+]B)
What does the gate look like? What does the expression look like?

## Slide 8: Example: Make the Karnaugh map and reduce the expression.
z | y | x | w | out
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | X
1 | 0 | 1 | 1 | X
1 | 1 | 0 | 0 | X
1 | 1 | 0 | 1 | X
1 | 1 | 1 | 0 | X
1 | 1 | 1 | 1 | X

## Slide 9: Creating a BCD to 7-Segment Display Driver
Download the BCD to 7-Seg Worksheet
Use the reduced logic from the Karnaugh Maps to create the circuit on Logisim (Use as few gates as possible, this may require some Boolean algebra.)